Version 1. 11/10/2023
Emilio J. Juarez-Perez, ejjuarezperez@unizar.es

## Schematic

## Bill of Materials
Amount	Part Type	Properties
1	ATmega328	Atmel microchip as found in Arduino UNO (Rev3) or equivalent
1	MCP4725 12-bit DAC	chip label MCP4725 Breakout; editable pin labels false; variant variant 2; pins 6
1	INA219 DC Current Sensor Breakout	variant variant 5
1	Basic FET N-Channel	package TO220 [THT]; type n-channel, IRLZ34N, IRLI540N
1	Ceramic Capacitor	voltage 6.3V; capacitance 100nF; package 100 mil [THT, multilayer]
2	1kΩ Resistor	bands 4; tolerance ±5%; package THT; resistance 1kΩ; pin spacing 400 mil
1	10kΩ Resistor	bands 4; tolerance ±5%; package THT; resistance 10kΩ; pin spacing 400 mil
1	Temperature Sensor (Thermistor)	resistance at 25° 10kΩ; package THT; type thermistor; thermistor type NTC
2	Screw terminal - 2 pins	pin spacing 0.197in (5.0mm); hole size 1.0mm,0.508mm; package THT; pins 2

## Perovskino Shield 2209EJJP
https://aisler.net/p/VEECBBJB

## Perovskino Shield 2304EJJP
https://aisler.net/p/SDRQAOGS
Update of the shield to accommodate various commercially available versions of MCP4725:

If employing the 5-pin Adafruit pin configuration, solder the pad connecting VGATE and pin 5.

## Perovskino Perfboard Implementation

## LSH-7320 Oriel Solar Simulator
For inquiries regarding a program to conduct EN50530 illumination cycle tests in the LSH-7320 LED-based Oriel Solar Simulator, please contact ejjuarezperez@unizar.es

## Figures

Figure: a) bread-, b) perf- and c) printed circuit- board (PCB) implementations of the perovskino shield.

Figure: front and back of the perovskino shield (early version 0).

Figure: printed box with banana plugs for the Arduino + Perovskino shield.